## Slide 1
NeSC: Self-Virtualizing Nested Storage Controller
Yonatan Gottesman • Yoav Etsion
Technion – Israel Institute of Technology
IO-Virtualization
Idea: the performance of Direct-IO with the isolation of Emulation
Virtualization Overheads
As devices get faster, software overheads get more significant
We must rethink the division of labor between hardware and software
NeSC
Combine SR-IOV with file isolation
Device enforces isolation
Prototype
We implemented NeSC storage controller on Xilinx FPGA
KVM/QEMU hypervisor
Hypervisor driver and management code
EXT4 extent based filesystem
Results
Latency
Throughput
Filesystem overheads
NeSC Objectives
Enable multiple VMs to directly access the storage device (Direct-IO)
Enforce file-level isolation at the hardware level
Separate control and data path to be filesystem agnostic
    Hypervisor creates isolation policy
    Hardware enforces policy on every access
Introduction
Design
Conclusion
Multiple VMs, single device? SR-IOV
PCIe interface specification
Multiple clients share the device VIA direct-IO
Hardware-level Isolation: extent trees
Virtio uses host filesystem to enforce isolation
Each VM attached to a file
Each file maintains logical to physical mapping with extent trees
Storage Blocks
NeSC
VM 1
VM 2
Inode
Extent-Header
Extent-Index
Extent-Header
Extent-Index
Extent-Index
Extent-Index
Extent-Header
Extent-Index
Extent-Index
Extent-Index
Extent-Header
Extent-Index
Extent-Index
Extent-Index
Storage Blocks
File Offset
LBA
Virtual Function
BAR
Physical Function
storage
Hypervisor
DMA
Virtual Function
BAR
DMA
BAR
DMA
VM
MUX
Translation Unit
VM
VLBA
PLBA